OPERATION OF IC PLATE 2 READER

Set up the type of plate required :-

1. Open the unit using the light grey slider on the side of the unit and push the red button       on the underside of the unit the display should show the IC PLATE 2 symbol.

2. Push the right hand button and the plate types will be shown.

The top line shows metal plate then pos or neg image and regular dot the fourth ikon is      for the normal calculation.

The second  line shows polyester plate then neg image and stochastic dot the fourth            Ikon  is  for the Fogra calculation

3.  The arrows allow you to move along and down the screen, the hand symbol to return to       the measurement mode

To operate any function the right hand button is the return key.

Measuring the plate

1. Open the unit using the light grey slider on the side of the unit.

2. Push the left hand button and the display should show the IC PLATE 2 symbol or a dot     percentage.

3. Using the clear target place the unit over the tint on the plate to be measured

4. Push down the unit and hold in position until the display (eg. DOT  12.4%) appears

5. You will note that there is no need to calibrate the unit this is done automatically as you      take the measurement, it is necessary however to have the unit calibrated on a regular       basis to maintain this function.